## Slide 1: Unit One: Greenhouse Care and Maintenance
Lesson One:
Materials and Equipment
Lesson Objectives
Identify plant materials and equipment that are commonly used in the greenhouse industry.
Examine common growing media and evaluate their use in plant production.
Discuss the importance of irrigation and the equipment associated with those systems.
Footer description area.

## Slide 2: Introduction
Today you are the manager of a greenhouse...
Shopping List – Think, Pair, Share Activity:
What materials and equipment are necessary to run a greenhouse operation?

## Slide 3: Materials and Equipment
Anvil and Blade Pruner
Hook and Blade Pruner
Bulb Planter
Cell Pack Containers
Hanging Basket
Nursery Container
Scoop Shovel
Square-Point Shovel
Sharpening Stone
Propagation Mat
Propagation Trays
Greenhouse Thermostat
Soil Moisture Meter
pH Testing Meter
Polyethylene Film
Shade Fabric
PVC Pipe
PVC Pipe Cutter
Greenhouse Production Items

## Slide 4: Anvil and Blade Pruner
http://www.original-lowe.com/uploads/tx_loeweproducts/7.107_offen.jpg
Anvil pruners cut by pushing a blade through a material.
At the end of the cut, the blade's cutting edge meets the anvil.

## Slide 5: Hook and Blade (Bypass) Pruners
http://www.gemplers.com/img/felco-classic-hand-F2-lrg.jpg
Bypass pruners have a blade sharpened on the outside edge that slides past a hook.
They make clean cuts, close to the stem but can't be used on branches larger than 1/2 inch in diameter.

## Slide 6: Bulb Planter
http://ace.imageg.net/graphics/product_images/pACE-959626dt.jpg
http://www.claringtonforge.com/media/catalog/product/cache/1/image/650x/9df78eab33525d08d6e5fb8d27136e95/i/m/image_65.jpg
A bulb planter is a hand tool that has an open-ended cone sharpened on its bottom edge.

## Slide 7: Cell Pack Container
http://www.torontonurseries.com/wp-content/uploads/2016/01/L-606-1.jpg
A container made of
cellular plastic.
Varies in size (width and depth)
Used for holding flowers or plants.

## Slide 8: Hanging Baskets
http://cdn.greenhousemegastore.com/images/uploads/12607_7026_popup.jpg
A hanging basket is a suspended container used for growing decorative plants.
Hanging baskets are normally made from wire with an impervious, usually plastic, lining to retain the contents.

## Slide 9: Nursery Container
Nursery containers have heavy-duty, wrap-around rims that are easy to handle and strong enough to pick up heavy plant material.
Superior drainage is engineered into both side and bottom drain designs. They typically come in black and are a minimum of a half-gallon in size.
http://cdn.greenhousemegastore.com/images/uploads/14395_5905_popup.jpg

## Slide 10: Scoop Shovel
https://www.ewingirrigation.com/media/catalog/product/c/o/corona_aluminum_scoop_shovel_ss68000_1.jpg
A scoop shovel is used to scoop and move large quantities of material at once, such as small rocks, sand, soil, etc.

## Slide 11: Square-Point Shovel
https://www.agriculturesolutions.com/images/stories/virtuemart/product/SPS30_1.jpg
Square-point shovels can perform many of the same functions as garden spades (ex: lawn edging, transplanting small bushes and trees, cutting sod and small roots, dividing perennials and trenching).
Sharp, flat tips of square points are also utilized more for digging in hard-packed soils that demand more force to penetrate.

## Slide 12: Sharpening Stone
http://ecx.images-amazon.com/images/I/41eC4CGczRL._SX300_.jpg
Sharpening stones are used to grind and hone the edges of steel tools and implements.

## Slide 13: Propagation Mat
http://cdn.greenhousemegastore.com/images/uploads/2376_2795_popup.jpg
These heated rubber mats are made so that planters containing seedlings can be placed on top of the mat.
When combined with a lighting system, many plants can be grown indoors using these mats.
Notes: In extreme cold, gardeners place a plastic cover over the planters/mats which creates a miniature greenhouse.
The constant and predictable heat allows people to garden in the winter months when it’s generally too cold for seedlings to survive.

## Slide 14: Propagation Trays
http://cdn.greenhousemegastore.com/images/uploads/1893_4510_popup.jpg
Propagation Trays provide extra depth for increased soil volume, allowing for a more mature plant and longer shelf life.
These are the most economical inserts for growers who do not use plug extractors or transplanters.

## Slide 15: Greenhouse Thermostat
http://media.qcsupply.com/catalog/product/cache/1/image/9df78eab33525d08d6e5fb8d27136e95/1/0/10004.jpg
http://cdn.greenhousemegastore.com/images/uploads/1476_1786_popup.jpg
Thermostats are used to detect or control conditions in the greenhouse.
Equipment in the greenhouse is turned on and off to reach the desired temperature set on the thermostat.

## Slide 16: Soil Moisture Meter
http://ecx.images-amazon.com/images/I/61GfDJbqWRL._SY355_.jpg
A soil moisture meter is an instrument for determining the percentage of moisture in a material (such as soil), which is commonly found by measuring its electrical resistivity.

## Slide 17: pH Testing Meter
A pH meter is a scientific instrument that measures the hydrogen-ion concentration (or pH) in a solution, indicating its acidity or alkalinity.
The pH meter measures the difference in electrical potential between a pH electrode and a reference electrode.
http://www.specmeters.com/assets/1/14/DimLarge/IQ-150-pH-Meter-ISFET-Probe.jpg

## Slide 18: Polyethylene Film
http://www.hyatts.com/eCom/images/B/B12052.jpg
Polyethylene film is a thick, flexible material that comes in sheets of various thickness (measured in mil) that can be used in single or double layers (for better insulation).
A quick and inexpensive option for growers.
Its translucency diffuses light well, bouncing the available sunlight and reducing shadows, both of which aid plant growth.
http://cdn.greenhousemegastore.com/images/uploads/2111_510_popup.jpg

## Slide 19: Shade Fabric
http://store.rimolgreenhouses.com/v/vspfiles/photos/shadeclothfinished-2.jpg
http://cdn.greenhousemegastore.com/images/uploads/2402_4034_popup.jpg
Shade fabric/cloth is a commercially available material for hanging over greenhouse glazing to cool it in summer months.
They are usually made of loosely woven polyester or aluminum and can be found in varying densities or degrees of shade from approximately 5% to 95%.

## Slide 20: PVC Pipe
http://www.villages-news.com/wp-content/uploads/2015/12/img_large_18243.jpg
Polyvinyl chloride, commonly abbreviated as PVC, is the third-most widely produced synthetic plastic polymer.
PVC comes in two basic forms: rigid (sometimes abbreviated as RPVC) and flexible.

## Slide 21: PVC Pipe Cutter
http://selectproductsltd.com/images/sizes/SEL22436_PVC_Pipe_Cutters.jpg
A PVC pipe cutter is a type of tool used to cut PVC pipe.
Besides producing a clean cut, the tool is often a faster, cleaner and more convenient way of cutting pipe than using a hacksaw.

## Slide 22: Materials and Equipment
Sphagnum Moss
Peat Moss
Perlite
Sand
Rice Hulls
Vermiculite
Coconut Coir
Peat Pots
Elle Pot
Rock Wool Growing Pots
Growing Media and Material

## Slide 23: Sphagnum Moss
http://www.recorpinc.com/images/moss/sphagnum-moss.jpg
Living vegetation gathered from the tops of swamps, bogs and marshes and then dried out
Has a very acidic pH, relatively sterile and lightweight
Excellent moisture-holding capacity

## Slide 24: Peat Moss
http://lghttp.17653.nexcesscdn.net/808B16/cdn_images/media/catalog/product/cache/1/thumbnail/9df78eab33525d08d6e5fb8d27136e95/p/s/pso100a.jpg
Partially decomposed vegetation gathered from swamps, bogs or marshes and then ground up
Found below the living sphagnum moss
Good source of nitrogen with a high moisture-holding capacity

## Slide 25: Perlite
http://garden.org/pics/2015-01-12/drdawg/12d404.jpg
A gray-white material derived from volcanic ash
Usually added to increase aeration in a growing media
Commonly used as media during propagation

## Slide 26: Sand
http://hydroponicgardening.com/wp-content/uploads/2015/05/CoarseSand600400.jpg
Not like the sand at a beach, this is finely ground stone
Contains the same elements as the parent material
Example: If the stone had high levels of calcium, the sand produced from that stone will have high levels of calcium.
Provides structure to growing media and increases drainage

## Slide 27: Rice Hulls
http://cdn.arbico-organics.com/images/uploads/1309000-m.jpg
By-product of rice production
Adds aeration to the growing media
Has a high moisture-holding capacity
Used in combination with other growing media
  not to be used independently

## Slide 28: Vermiculite
http://cdn2.hubspot.net/hub/137863/file-522660781-jpg/images/vermiculite.jpg
Derived from heat- treated mica ore
Very lightweight with a neutral pH
Commonly used in media for seedlings
High moisture-holding capacity

## Slide 29: Coconut Coir
http://www.soilless.org/wp-content/uploads/2016/04/CoirBlock_soillessorg.jpg
Made from the husk of a coconut
Hairy, fibrous material that is high in phosphorous and potassium
Commonly used in hanging baskets
High moisture-holding capacity with little shrinkage

## Slide 30: Peat Pots
https://laidbackgardener.files.wordpress.com/2015/04/20150414c.jpg
Biodegradable plastic containers made from compressed peat moss
Can be transplanted directly into a new container
Reduces root damage or stress
Removes the need for conventional plastic containers

## Slide 31: Elle Pots
http://hort.ufl.edu/woody/images/ellepot.jpg
Biodegradable paper containers made from cellulose
Can be transplanted directly into a new container
Reduces root damage or stress
Removes the need for conventional plastic containers

## Slide 32: Rock Wool Growing Cells
http://ecx.images-amazon.com/images/I/51nlxtWAe4L.jpg
Made from a mixture of inorganic materials
Weathers with time but not fully biodegradable
Can be transplanted directly into a new container
Reduces root damage or stress
Removes the need for conventional plastic plug trays

## Slide 33: Materials and Equipment
Hose Punch
Hose Repair Coupling
Hose-End Repair Fitting
Hose-End Sprayer
Hose-End Washer
Impulse Sprinkler
Irrigation Drip Emitter
Irrigation Timer
Irrigation Tape
Polyethylene Pipe
Spaghetti Tubing
Mist Nozzle
Oscillating Sprinkler
Siphon Proportioner
Solenoid Valve
Backflow Preventer
Fertilizer Injector
Water Breaker
Watering and Irrigation Equipment

## Slide 34: Hose Punch
https://www.plumbingsupply.com/images/drip-deluxe-tubing-punch.jpg
Tool used to create small holes in plastic hose used in irrigation systems
The hole created by the hose punch is where irrigation heads can be inserted.

## Slide 35: Hose Repair Coupling
http://www.easy-irrigation.co.uk/images/brass-hose-joiner-main.jpg
A connector on the end of a hose to connect (or couple) it with another hose or an irrigation sprinkler.

## Slide 36: Hose-End Repair Fitting
http://ace.imageg.net/graphics/product_images/pACE3-14560784enh-z8.jpg
A device attached to the end of the hose to facilitate connection.

## Slide 37: Hose-End Sprayer
http://1274ym4fbva545shrh1giu44.wpengine.netdna-cdn.com/wp-content/uploads/2013/03/hose-end-sprayer.jpg
A sprayer that fits on the end of a garden hose. It is used to apply fertilizer or other chemicals to the lawn or garden.
The water from the hose mixes with the contents of the sprayer to dilute the contents.

## Slide 38: Hose-End Washer
http://ace.imageg.net/graphics/product_images/pACE3-7931135enh-z8.jpg
Controls the pressure and stream of water coming out of the hose

## Slide 39: Impulse Sprinkler
http://www.shopsteins.com/magento/media/catalog/product/cache/1/image/9df78eab33525d08d6e5fb8d27136e95/4/1/417837_detail.jpg
This is a type of irrigation sprinkler in which the sprinkler head, driven in a circular motion by the force of the outgoing water, pivots on a bearing on top of its threaded attachment nut.

## Slide 40: Irrigation Timer
http://images.lowes.com/product/converted/046878/046878289543lg.jpg
An irrigation controller is a device to operate automatic irrigation systems such as lawn sprinklers and drip irrigation systems.
Most controllers have a means of setting the frequency of irrigation, the start time and the duration of watering.

## Slide 41: Irrigation Tape
http://www.irrigation-tools.com/products/2-2-1.jpg
Irrigation or drip tape is a type of thin-walled dripperline used in drip irrigation.
It’s sold flat, on reels containing several thousand feet.
The wall thickness typically ranges from 4 to 25 mils (0.1–0.6 mm).
Water exits the tape through emitters/drippers. Typical emitter spacing ranges from 6 to 24 inches (150-600 mm).

## Slide 42: Polyethylene Pipe
http://www.greenhousemegastore.com/product/black-polyethylene-tubing/greenhouse-irrigation-fittings-hardware
Used in greenhouse and various irrigation systems
Polyethylene pipe is chemical resistant, so fertilizer and pesticide can travel through the pipe without contaminating other water systems.

## Slide 43: Spaghetti Tubing
https://www.berryhilldrip.com/images/T/spot%20spitter.jpg
Spaghetti tubing is a very fine plastic tubing used in drip irrigation, typically in gardens and greenhouses, with a small inside diameter, which may be 0.05" or smaller.
The end of the tube may have a plastic or lead weight to hold the tube in a pot.
Notes: Spaghetti tubing is inserted directly into the supply tubing.
The flow is regulated by the inside diameter of the tube and the length of tubing used.
The smaller the diameter and the longer the tube, the greater the friction loss, thus reducing the pressure and flow.

## Slide 44: Mist Nozzle
http://ecx.images-amazon.com/images/I/51CWEAtwioL._SY300_.jpg
Misting is a technique for minimizing plant moisture loss by controlled, periodic wetting of the foliage of cuttings which are being rooted.
This technique is helpful for rooting leafy cuttings.

## Slide 45: Oscillating Sprinkler
http://www.waterirrigation.co.uk/media/catalog/product/cache/2/image/1000x1000/9df78eab33525d08d6e5fb8d27136e95/5/4/541.jpg
A sprinkler that has a bar that tips back and forth. It delivers a fine spray to a large area.
It can be set for square or rectangular areas.

## Slide 46: Siphon Proportioner
http://www.ultimatewasher.com/images/sm/stream-injector_lg.jpg
Easily and accurately applies a consistent rate of soluble fertilizer to lawn, garden or greenhouse plants
Attaches to a standard hose fitting and offers built-in back flow prevention should pressure fail
Brass body ensures durability and spring filter eliminates clogging

## Slide 47: Backflow Preventer
http://backflowparts.com//wp-content/gallery/watts/008.jpg
A backflow prevention device is used to protect potable water supplies from contamination or pollution due to backflow.
Water pressure may fail or be reduced when a water main bursts, pipes freeze or there is unexpectedly high demand on the water system.
Reduced pressure in the pipe may allow contaminated water from the soil or from other sources to be drawn up into the system.

## Slide 48: Solenoid Valve
http://www.valveandactuatorcompany.co.uk/cms_images_products/160_1_large.jpg
A solenoid valve is an electromechanically operated valve. The valve is controlled by an electric current through a solenoid.
Their tasks are to shut off, release, dose, distribute or mix fluids. They are found in many application areas such as automatic irrigation systems.

## Slide 49: Fertilizer Injector
http://lghttp.17653.nexcesscdn.net/808B16/cdn_images/media/catalog/product/cache/1/thumbnail/9df78eab33525d08d6e5fb8d27136e95/w/m/wmx200a.jpg
Fertilizer injectors are devices used to apply water-soluble fertilizers, pesticides, plant growth regulators, wetting agents and mineral acids during crop production.
They are a vital part of modern greenhouse or nursery operations.

## Slide 50: Water Breaker
http://cdn3.volusion.com/atyw2.hvqa2/v/vspfiles/photos/DC-10-22368-2.jpg
Designed to offer a soft, aerated flow of water so the force of the water will not damage plants or disturb the soil

## Slide 51: Review
Let’s try that list again…
Shopping List: Reflect and Summarize
Create a new list using the items identified in today’s lesson.
You can only select 10 items.
Include what the item does and why you need it.
Example: Polyethylene Film – A strong, clear plastic that will be used to build the walls and roof of the greenhouse.