## Slide 1: Equipment and Facility Cleaning and Inspection

## Slide 2: Objectives
Identify sanitation and cleanliness procedures
Create a routine maintenance program
Identify and maintain Sanitation Standard Operating Procedures (SSOP)
Identify regulations and regulatory agencies used in the food processing industry

## Slide 3: Video
Sanitizing the Kitchen

## Slide 4: Cleaning
involves physically removing food, soil, or other contaminants from a surface usually with the aid of a detergent, water and some muscle power.
Cleaning agents include detergents, solvents, abrasive cleaners, acid cleaners or some combination.
Read the manufacturer’s product description to select the cleaning agent that best meets your cleaning needs.

## Slide 5: Steps in Cleaning
  Put items that are clean away including food and utensils
  Extra food/ leftovers should be put in plastic containers then placed in the refrigerator to be eaten later
  Throw away trash
  Use the sink to clean dishes: Plug the sink and pour some soap, add hot water to the sink.

## Slide 6: Steps in Cleaning
  Place silverware in the soapy water, scrub and clean the silverware, rinse, set in the dish dryer to air dry
  Follow step five for bowls, plates, glasses, and pans
  Once the dishes are clean, wipe down every kitchen surface. Use a chemical cleaner and a clean rag to clean surfaces
  After dishes are dried put them away in clean storage areas

## Slide 7: Sanitizing
takes cleaning a step further by reducing the number of bacteria and other microorganisms.
Sanitizing can help prevent disease transmission, contamination and/or spoilage.
Sanitizing, however, is not a substitute for cleaning and improperly cleaned surfaces will reduce the effectiveness of the sanitizers

## Slide 8: Types of sanitizing
Heat Method
  With the heat method, a clean object is exposed to enough heat to kill bacteria.
Chemical Method
  With the chemical method, a clean object is immersed in or sprayed with a sanitizing solution.

## Slide 9: Sanitizing using a three-compartment
Scrape and pre-rinse.
Scrub and wash in the first compartment.
Rinse in the second compartment.
Sanitize in the third compartment by using a chemical sanitizer or by heating the water to 170 °F.
Air dry. As you may know air drying is more sanitary than towel drying, because of the lower chance of cross-contamination.
Change the water frequently. For the chemical method, use a chemical test kit to confirm that the sanitizer is active. For the heat method, use a thermometer to check the temperature of the water

## Slide 10: Sanitizing equipment
Unplug the equipment.
Disassemble the equipment.
Wash, rinse, and sanitize the removable parts in a three-compartment sink.
Wash and rinse the stationary parts.
Sanitize any areas that touch food

## Slide 11: Sanitizing using a dish machine
Scrape, separate, and pre-rinse.
Place cups, bowls, and plates on the rack.
Make sure the spray arms, soap trays, and curtains are clean.
Shut the drain valves and fill the tank.
Check the detergent, rinse dispenser, and sanitizer.
Turn the heat and the machine on.
Check the temperatures and gauges. Record the temperatures in the log.
Prewash (80–100 °F).
Wash (140–180 °F).
Rinse (170–180 °F).

## Slide 12: Preventative Maintenance
maintains the processing environment to optimize production and minimize food safety risks and equipment failures

## Slide 13: How do I create my own preventative maintenance program?
Gather data and create a master list of equipment
Identify maintenance tasks for each item
Determine the frequency of each task
Records are required to manage the Preventative Maintenance Program
Develop a policy for temporary repairs

## Slide 14: Gather data and create a master list of equipment
Food handling storage
Processing
Packaging
Air-handling units
HVAC
Compressors
Boilers
Storage silos
Temperature and humidity controls
Water backflow preventers.
Doors
Windows
Carts
Dollys
Dock levelers
Dock pads

## Slide 15: Identify maintenance tasks for each item
Consider the manufacturer’s recommendations, equipment history, and past experiences. Tasks could include inspecting, monitoring, lubricating, and replacing parts.
Condition monitoring (actions that detect failures) - should include equipment, facilities, structure, and grounds. Monitoring can be completed by critical scheduling protocols, daily work orders, and employee observations.
Predictive maintenance (actions that prevent failures) - inspects the condition of the equipment and determines failure based on the information gathered.

## Slide 16: Determine the frequency of each task
Factors to consider that affect frequency, including manufacturer recommendations, how often the equipment is used, criticality of the equipment, and how the equipment impacts food safety and quality

## Slide 17: Records are required to manage the Preventative Maintenance Program
Routine work orders can be printed and given to mechanics and completed orders can be retained for the required period.
There are software programs to help monitor work orders. They can also be managed through spreadsheets, checklists, forms, etc.

## Slide 18: Develop a policy for temporary repairs
Temporary repair materials, such as duct tape, wire, string, cardboard, etc., should only be in place until a permanent repair can be made.
Some plants do not allow for temporary repairs.
If they are allowed, clear guidelines must be established.

## Slide 19: Five SSOP Requirements
The plant must have a written plan describing daily procedures the establishment will conduct before and during operations and the frequency at which they will be conducted to prevent direct contamination or adulteration of product(s)

## Slide 20: Five SSOP Requirements
  The plan must be signed and dated by an official with the overall on-site authority or a higher level official of the establishment. The plan must be signed upon initiation and when modified.

## Slide 21: Five SSOP Requirements
The plan must identify pre-operational sanitation procedures and distinguish them from sanitation activities to be carried out during operations.

## Slide 22: Five SSOP Requirements
  The written SSOP must identify the individuals who are responsible for implementing and maintaining daily sanitation activities.

## Slide 23: Five SSOP Requirements
The establishment must maintain daily records that demonstrate they are implementing the sanitation procedures outlined in their SSOP plan, including corrective action.

## Slide 24: Pre-Operational Sanitation
General equipment cleaning. All equipment, used for processing will be cleaned and sanitized prior to starting production
  Establish cleaning procedures
  Implementation, Monitoring and Recordkeeping
  Corrective Actions

## Slide 25: Pre-Operational Sanitation
Cleaning of facilities, including floors, walls and ceilings
  Cleaning procedures
  Cleaning Frequency
  Implementation, Monitoring and Recordkeeping
  Corrective Actions

## Slide 26: Operational Sanitation
Food processing operations.
  Food processing must be performed under sanitary conditions to prevent direct and cross-contamination of ingredients.
  Established personal hygiene procedures for employees handling food and processing products
  Established procedures for handling and storage of food products
    Separation of
      Raw meat from cooked meat
      Raw meat/ fish from produce that will not be cooked before consumption
  Established procedures for insect and rodent control
  Established procedures for processing different product clean-up
  Implementation, Monitoring, and Record Keeping

## Slide 27: FSIS
Food Safety Inspection System
FSIS is the public health system in USDA (United States Department of Agriculture) responsible for ensuring that the nation’s supply of meat, poultry and egg products are safe, wholesome, and correctly label and packaged.
FSIS inspectors are expected to be present in every establishment every day.
http://www.defendingfoodsafety.com/tags/fsis/

## Slide 28: FDA
Food and Drug Administration
FDA is responsible for protecting the public health by assuring the safety, efficacy and security of human and veterinary drugs, biological products, medical devices, our nation’s food supply, cosmetics, and products that emit radiation. FDA inspectors visit non-meat establishments once a year or every other year.
www.fda.gov/

## Slide 29: DHHS
Department of Health & Human Services
  The Department of Health and Human Services (HHS) is the United States government’s principal agency for protecting the health of all Americans and providing essential human services, especially for those who are least able to help themselves.
http://www.mirusmedia.net

## Slide 30: DHS
Department of Homeland Security
The Department of Homeland Security has a vital mission: to secure the nation from the many threats we face.
This requires the dedication of more than 240,000 employees in jobs that range from aviation and border security to emergency response, from cybersecurity analyst to chemical facility inspector.
Our duties are wide-ranging, but our goal is clear - keeping America safe.
wikipedia.org

## Slide 31: CDC
Centers for Disease Control
Collaborating to create the expertise, information, and tools that people and communities need to protect their health – through health promotion, prevention of disease, injury and disability, and preparedness for new health threats.
foodpoisonjournal.com

## Slide 32: EPA
Environmental Protection Agency
The mission of EPA is to protect human health and the environment.
ncbm.org

## Slide 33: Review
Create a model of how the cleaning and sanitizing process works or how the regulatory agencies work together to protect the U.S. food system